## Slide 2: Turbulent Transport in the Atmospheric and Oceanic Mixed Layer Under Convective Conditions Studied with Large-Eddy Simulation
Siegfried Raasch
Institut für Meteorologie und Klimatologie Leibniz Universität Hannover

## Slide 3: LES applications at IMUK
dust devils
roll convection
canopy layer effects
cloud droplet growth
entrainment
urban canopy layer
turbulence effects on aircrafts

## Slide 4: Ocean-LES applications at Yonsei University, Seoul
Noh, Y., W.-G. Cheon and S. Raasch (2003): The role of preconditioning in the evolution of open-ocean deep convection, J. Phys. Oceanogr., 33, 1145-1166
Noh, Y., H.S. Min and S. Raasch (2004): Large-eddy simulation of the ocean mixed layer: The effects of wave breaking and Langmuir circulation, J. Phys. Oceanogr., 34, 720-735
Min, H.S. and Y. Noh, 2004: Influence of the surface heating on Langmuir circulation. J. Phys. Oceanogr., 34, 2630-2641
Noh, Y., Kang, I.S., Herold, M. and S. Raasch (2006): Large-eddy simulation of particle settling in the ocean mixed layer, Phys. of Fluids, 18, 085109
Noh, Y., G. Goh, S. Raasch and M. Gryschka (2009): Formation of a diurnal thermocline in the ocean mixed layer simulated by LES, J. Phys. Oceanogr., 39, 1244-1257
Noh, Y., G. Goh and S. Raasch (2010): Examination of the mixed layer deepening process during convection using LES, J. Phys. Oceanogr., 40, 2189-2195
Noh, Y, G. Goh and S. Raasch (2011): Influence of Langmuir Circulation on the Deepening of the Wind-Mixed Layer, J. Phys. Oceanogr., 41, 472-484

## Slide 6
3D-turbulence characteristics
Energy production and dissipation on different scales
  Large scales (L): shear and buoyant production
  Small scales (h): viscous dissipation
Large eddies: 103 m, 1 h L Small eddies: 10-3 m, 0.1 s h
Garratt (1992)

## Slide 7
Turbulence characteristics
Number of gridpoints for a 3D simulation of turbulence:
Turbulence simulation covering all scales of turbulence is called a Direct Numerical Simulation (DNS).

## Slide 8: LES Principals
RANS: ensemble average
local concentration time series
local concentration time series
building
building
after Schatzmann and Leitl (2001)
LES: volume average
D
smooth result
fluctuations (u, c)
x
z
x
z
subfilter-scale
resolved scale

production
inertial subrange
dissipation
critical concentration level

## Slide 9
Volume averaged NS-equation for a non-divergent, Boussinesq fluid:
volume average (resolved scale)
subgrid-scale fluctuations (subgrid scale, SGS)
volume balance approach
(Schumann, 1975):
transport by large eddies
transport by small eddies
LES Principals – Model Equations (I)

## Slide 10: Short Introduction to LES (III)
LES SGS-turbulence parameterization (after Deardorff):

## Slide 11
horizontally averaged profiles of a typical convective atmospheric boundary layer as simulated by LES
mixed layer
entrainment zone
inversion
potential temperature in K
Sensible heatflux in K ms-1
height in m
SGS
resolved
w´q´
parameterized
A Simple Example: Convection Above a Homogeneous Surface

## Slide 12
spectral energy distribution
A Simple Example: Convection Above a Homogeneous Surface

## Slide 13: A Simple Example: Convection Above a Homogeneous Surface
LES-setup:
homogeneously heated surface, temperature inversion at z = 800 m, domain size: 2 * 2 km2, D = 50 m cyclic horizontal boundary conditions
particles = passive tracers
colour ~ buoyancy: ↑ ↓
diameter ~ |vertical velocity|
isosurface of liquid water content (cumulus cloud)

## Slide 14
domain size: 4 * 4 km2
grid spacing: D = 2m
grid points: 109
color: buoyancy: red: pos., blue: neg.
dust devils
horizontal cross section at z = 20m
An Advanced Example: Coherent Structures in a Highly Resolved Convective Boundary layer
Raasch and Franke, 2011: J. Geophys. Res., 116, D1612.

## Slide 15: PALM - Overview
first version 1997, continously developed since then, under GPL
written in FORTRAN 95 / 2003
very high performance and scalability on all state-of-the-art parallel architectures
one code for atmosphere and ocean
PArallelized LES Model

## Slide 16: PALM – A PArallelized LES Model Features / Numerics
central finite differences
cartesian staggered grid
topography (cartesian or immersive)
non-cyclic horizontal boundary conditions + turbulent inflow
Runge-Kutta 3rd-order timestep scheme
FFT- or multigrid-method for solving the Poisson-equation
various high order advection schemes available (default: Wicker-Skamarock)
canopy model
cloud physics (two moment scheme after Seifert and Beheng)
embedded complete Lagrangian particle model (dispersion modelling, cloud droplets, graphics)
ocean-version with salinity (can be coupled with atmosphere)
large-scale forcing and nudging
online data analysis, all output in netCDF format
for further details see:
http://palm.muk.uni-hannover.de
Maronga et al., 2015: Geosci. Model Dev. Discuss.,
DOI: 10.5194/gmdd-8-1539-2015

## Slide 17: Turbulent Transport Above Leads
1 km
2 km
sea smoke
-25 0C
-2 0C

## Slide 18
ice
ice
inversion layer
convection
stable / neutral
stable / neutral
wind
zi =250 m
lead
unstable
20 km
1 km
-24 0C
-3 0C
-24 0C
entrainment
very complex structure
very few data
difficult to parameterize
the triggered convection affects wind profile, entrainment, surface fluxes, …
Questions:
How to parameterize lead induced turbulence in larger scale models?
How is entrainment effected?
How does surface heating depend on lead width?
Boundary Layer Above a Lead

## Slide 19: Leads: Effects of Grid Resolution
w
lead
lead
lead
lead
ρcpw'θ'
ρcpw'θ'
lead
lead
lead
lead
with increasing resolution onset of convection moves to the upstream edge
pronounced heat flux maximum disappears with higher resolution
contributions of SGS-fluxes become negligible
Δ = 2 m
Δ = 1 m
Δ = 0.5 m
Δ = 0.25 m
wind direction

## Slide 20: Leads: Effects of Upstream Turbulence
upstream coherent structures trigger the convection pattern above and behind the lead
instantaneous vertical velocity in m/s
xy-cross section at z = 10 m
laminar inflow
turbulent inflow
lead

## Slide 21
sensible heatflux (W/m2)
improved temperature field
pot. temperature (K)
sensible heatflux (W/m2)
flux
too large
METRAS new improved closure
Flow Over Leads: PALM - METRAS Comparison
Using LES data for turbulence parameterizations in larger scale models
PALM
METRAS
local closure
unstable
strongly stable
pot. temperature (K)
pot. temperature (K)
pot. temperature (K)
weakly stable
sensible heatflux (W/m2)
sensible heatflux (W/m2)
flux too low
plume is not tilted
METRAS
non-local closure
Lüpkes et al., 2008: Modelling Convection over Arctic Leads. J. Geophys. Res., 113.

## Slide 22
Leads: Relation Between Lead Width l and Surface Heatflux
PALM results
The Esau (2007) study appeared to have several drawbacks.
Most important one: ratio l / domain width was not held constant!
Esau, 2007: Amplification of turbulent exchange over wide Arctic leads. J. Geophys. Res., 112.
No background wind was used.
mean surface heat flux in K m/s
z
lead
lead
lead
Notes: Kommentare:
Gestrichelte Kurve weglassen, verwirrt nur (oder ausführlicher auf Extra-Folie erklären)
Nur auf Nachfrage auf die unterschiedliche Wärmeflussbestimmung eingehen
22

## Slide 23
Leads: Relation between Lead Width l and Surface Heatflux Using l / domainwidth = const.
optimum resolution
New result: linear decrease of surface flux with a scale jump at l ~ 5000m.
Gryschka et al., 2015: Turbulent exchange above leads studied with high resolution LES. In preparation.
mean surface heat flux in K m/s

## Slide 24
For broader leads, flow convergence no more appears at the center of the lead
overall circulation is weakened, which explains the scale jump
λ = 5000 m
λ = 25000 m
Leads: Dependence of Flow Pattern on l
temporally averaged vertical velocity in m/s
Notes: Vertikalgeschwindigkeit in m/s fehlt!
Hiernach Fazit einbauen!
24

## Slide 25
400 km
Satellite image Terra-Modis during a CAO on 23.4.2002 / Davis Strait
situation requires non-cyclic boundary conditions along x
Organized convection during cold air outbreaks

## Slide 26
previous LES-results: rolls only if zi/L < 20 (weakly convective, “shear driven”)
rolls in nature are frequently observed with zi/L > 20
geostrophic wind
2d-heterogeneities
1d-heterogeneity (along wind)
Gryschka et al., 2008: Geophys. Res. Lett.
PALM simulations
D = 50m
8000*1200*200
grid points
liquid water path
y [km]
Organized convection during cold air outbreaks

## Slide 27
...
geostrophic
wind
400 km
Simulation with observed ice cover (from Terra-Modis satellite)
400 km
satellite image Terra-Modis during a CAO on 23.4.2002 / Davis Strait
Organized convection during cold air outbreaks
Question: Is there any additional heat transport due to the organized convection (rolls)?

## Slide 28
Heat transport by rolls:
rolls do not change the total transport of heat
roll transport
total transport
y = 80 km
Gryschka et al., 2014: J. Geophys. Res, 119.
Organized convection during cold air outbreaks

## Slide 29
Motivation for a coupled ocean-atmosphere LES
  Convective structures in ocean and atmosphere might interact and effect the overall heat exchange between the interface.
  However the turbulence is organized on largely different spatial and time scales in each media and influenced by complex physical processes at the interface.
  The technical development was motivated (payed) by Igor Esau (NERSC, Bergen), Yign Noh (Yonsei Univ., Seoul), and Jong-Hwan Yoon (RIAM, Kyushu Univ., Fukuoka)

## Slide 30: PALM equations (atmosphere)
momentum
liquid water potential temperature
specific humidity

## Slide 31: PALM equations (ocean)
Density r = r(S,q,ph) is calculated from the equation of state for seawater using the algorithm from Jackett et al. (2006)
momentum
potential temperature
salinity

## Slide 32: PALM SGS-Model
SGS-parameterization after Deardorff:
in ocean

## Slide 33: Ocean-Atmosphere Coupling in PALM: General Method
atmosphere to ocean coupling through Prandtl-Monin-Obukhov sublayer (constant flux layer)
ocean to atmosphere coupling through flux conservation
variables implemented: momentum, heat, humidity/salinity
no precipitation effects
wave effects at the interface are not accounted for (z0 ~ u*2 is implement)
q(zp), q(zp)
u(zp)
u(z0)=0
q(z0), q(z0)=qs
Prandtl-layer
q(top)ocean

## Slide 34: Ocean-Atmosphere Coupling: Flux Equations
ocean heat flux depends on atmospheric sensible AND latent heat flux (evaporation)
increase of salinity due to evaporation by salinity flux (after Steinhorn, 1991: JPO)
momentum

## Slide 35: Ocean-Atmosphere Coupling: Technical Realization (I)
1-1, or n-m coupling can be used
boundary information is exchanged after given time intervals (120 s)
before the coupling, each model can run seperately in order to allow for development of quasi-steady turbulence (different spin-up times in atmosphere and ocean)
pre-run ocean
pre-run atmosphere
atmosphere
ocean
time
0
coupled run
1
2
3

## Slide 36: Ocean-Atmosphere Coupling: Technical Realization (II)
communication between the two models is realized with MPI
MPI-2 intercommunicators allow to couple two different executables,
however the full MPI-2 standard is hardly available
MPI-1 starts only one executable, splits the total number of processors and calls the different models as subroutines
mpiexec -np8 palm &
mpiexec -np8 palm &
mpiexec -np16 palm
8 processors
8 processors

## Slide 37
Esau, 2014: Indirect air-sea interactions simulated with a coupled turbulence-resolving model. Ocean Dynamics, 64, 689-705.
Coupled Simulations: Shear Free Convection (I)
salinity
potential
temperature
first simulations with PALM in coupled mode
initial conditions

## Slide 38
Coupled Simulations: Shear Free Convection (II)
mean profiles in „equilibrium state“
pot. temperature
total heat flux
momentum flux
humidity/salinity flux
humidity/salinity change
buoyancy flux

## Slide 39
Coupled Simulations: Shear Free Convection (III)
instantaneous density
fluctuations after 20h
most co-variated patterns (first eigenvector) of the ABL-OML system
questions / problems:
  Why do structures in atmosphere and ocean have the same scale?
  Do the coupled organized structures enhance the energy transport?

## Slide 40
Cold Air Outbreaks: Effects on the OML Transport? (I)
y = 25 km
domain size is too large for a fully coupled simulation
cyclic ocean domain is driven with atmospheric fluxes averaged along x
averaged surface fluxes and flow at y = 25 km
flow convergence and cooling at different positions may be unfavourable to create an ocean circulation
Hypothesis:
stationary atmospheric circulations may induce a corresponding circulation in the ocean

## Slide 41
Cold Air Outbreaks: Effects on the OML Transport? (II)
initial profiles in ocean:
vertical cross sections after 65 h, averaged along x
after 65 h of heterogeneous forcing only very weak circulations are present
surface wind field seems to be the driving force

## Slide 42
Cold Air Outbreaks: Effects on the OML Transport? (III)
vertical cross sections without Langmuir circulation
What happens in case of Stokes drift?  onset of a strong Langmuir circulation
vertical cross sections with Langmuir circulation
So far, no direct signs for coupled atmosphere ocean circulations / interactions under convective conditions

## Slide 43: Summary / Comments
LES is a valuable tool for studying turbulent boundary layer processes
Compared to the atmospheric boundary layer, there are still only few LES applications for the OML so far
Coupled ocean-atmosphere LES are still at the very beginning, and it is unclear, under which conditions a coupling really makes sense
(PALM would be a suitable tool for such studies, so if you have any idea …)

## Slide 44
PALM group at IMUK in front of the Cray XC-40 at HLRN (May 2014)
Fabian Hoffmann
Dr. Christoph Knigge
Dr. Björn Maronga
Dr. Rieke Heinze
Simon Ward
Jens Fricke
Sebastian Giersch
Lennart Böske
Helge Knoop
Marius Keck
Manuel Dröse
Dr. Matthias Sühring
Farah Kanani
Prof. Siegfried Raasch
45000 cores 1.4 PFlop/s

## Slide 45: Thank You!